## Slide 1: The Fundamental of Mobile Robot
Machine Perception and Interaction Group (MPIG)
http://www.mpig.com.cn
szl@mpig.com.cn

## Slide 2
All the codes and slides accompanying the course are open-source
https://github.com/sunzuolei/robot
https://git.oschina.net/samuel/rob

## Slide 3
Localization with Histogram Filter

## Slide 4
Our robot has no clue where it is.

## Slide 5
GPS-liked localizer is not reliable.
We need sensors and the algorithms
for data cooking.
Our robot has no clue where it is.

## Slide 6
Let's assume there are 3 different landmarks in the world. they all look alike, so they're not distinguishable, but robot can distinguish the door from the non-door area--from the wall.

## Slide 7
Uniform function assigns equal weight to every possible place where the robot might be.
bel stands for belief. You may treat it as probability.

## Slide 8
By sensing with a camera, the robot knows that it is now located, likely, next to a door.

## Slide 10
Robot moves to the right by a certain distance. And It knows roughly how far it moved.

## Slide 11
The belief is shifted according to the motion. Now, robot motion is somewhat uncertain. We can never be certain where the robot moved. So these bumps are a little bit flatter than they were.
Convolution

## Slide 12
The robot senses again with its camera.

## Slide 13
How will the belief like?

## Slide 14
The robot has localized itself!!

## Slide 15
It is a core aspect of
localization especially
of mobile robot!

## Slide 16
Prior
Observation model / Sensor model
Posterior

## Slide 17
Prior
The probability before considering data (measurement)
Posterior
The probability after data (measurement) has been taken.

## Slide 18
Prior
Observation model / Sensor model
Posterior
Posterior
Process model / Motion model
Observation model / Sensor model

## Slide 19
Prior
Observation model / Sensor model
Posterior
Posterior
Process model / Motion model
Observation model / Sensor model
Update / Measurement update
Predict / Process update
Update / Measurement update

## Slide 20
Update / Measurement update
Predict / Process update
Prior
Posterior

## Slide 21
A world with 5 different cells or places
What is the probability of any of those x's?

## Slide 22
A world with 5 different cells or places
What is the probability of any of those x's?
0.2
The total probability equals 1

## Slide 23
A world with n different cells or places
What is the probability of any of those x's?
…

## Slide 24
A world with n different cells or places
What is the probability of any of those x's?
…
1/n
Let’s implement this！

## Slide 25
…
P1
OR
What’s the difference?
Are they problematic?

## Slide 26
…
P1
Explanation The size of the indicated variable or array appears to be changing with each loop iteration. Commonly, this message appears because an array is growing by assignment or concatenation. Growing an array by assignment or concatenation can be expensive. For large arrays, MATLAB must allocate a new block of memory and copy the older array contents to the new array as it makes each assignment. Programs that change a variable's size in this way can spend most of their run time in this inefficient activity.
For the same reasons, there is significant overhead in shrinking an array or in changing the size of a variable on each iteration.

## Slide 27
…
P1

## Slide 28
Now that we can establish the robot's initial belief about its location in the world, we want to update these beliefs given a measurement from the robot's sensors.
0.2
0.2
0.2
0.2
0.2

## Slide 29
Let's assume 2 of those cells are colored red whereas the other 3 are green.
0.2
0.2
0.2
0.2
0.2

## Slide 30
Sensors are incorrect, so we do not want to multiply the green cell probability by zero. Instead, we multiply it by 0.2!
0.2
0.2
0.2
0.2
0.2
Red cell * 0.6
Green cell *0.2

## Slide 31
What are the probabilities that the robot is in a red cell and the green cell?
0.2
0.2
0.2
0.2
0.2
Red * 0.6
Green *0.2

## Slide 32
Find the probability for each cell by multiplying the previous by the new factor, whose value depends on the color of the cells.
0.2
0.2
0.2
0.2
0.2
Red * 0.6
Green *0.2
0.04
0.12
0.12
0.04
0.04

## Slide 33
Is this a valid probability distribution?
0.2
0.2
0.2
0.2
0.2
Red * 0.6
Green *0.2
0.04
0.12
0.12
0.04
0.04

## Slide 34
NO! they do not add up to one.
0.2
0.2
0.2
0.2
0.2
Red * 0.6
Green *0.2
0.04
0.12
0.12
0.04
0.04
0.04*3+0.12*2 = 0.36

## Slide 35
How can we normalize it?
0.2
0.2
0.2
0.2
0.2
Red * 0.6
Green *0.2
0.04
0.12
0.12
0.04
0.04
0.04*3+0.12*2 = 0.36

## Slide 36
0.2
0.2
0.2
0.2
0.2
Red * 0.6
Green *0.2
0.04
0.12
0.12
0.04
0.04
0.04*3+0.12*2 = 0.36
1/9
1/3
1/3
1/9
1/9
Divide each of them by the sum!

## Slide 37
0.2
0.2
0.2
0.2
0.2
Red * 0.6
Green *0.2
0.04
0.12
0.12
0.04
0.04
1/9
1/3
1/3
1/9
1/9
Which is prior and posterior?

## Slide 38
0.2
0.2
0.2
0.2
0.2
Red * 0.6
Green *0.2
1/9
1/3
1/3
1/9
1/9
Prior
Posterior
The posterior distribution of robot being at place x_i given measurement Z.
Conditional probability

## Slide 39
Often, random variables carry information about other random variables. Suppose we already know that Z ’s value is z, and we would like to know the probability that X’s value is x conditioned on that fact.
Conditional probability

## Slide 40
0.2
0.2
0.2
0.2
0.2
Red * 0.6
Green *0.2
1/9
1/3
1/3
1/9
1/9
Prior
Posterior
Observation model
Z
Let’s implement this！

## Slide 41
P2

## Slide 42
P2

## Slide 43
P2

## Slide 44
P2

## Slide 45
Prior

## Slide 46
Posterior

## Slide 48
Let’s modify the code to deal with multiple measurements!
Red * 0.6
Green *0.2
Z
Green* 0.6
Red *0.2
Z

## Slide 49
P3

## Slide 50
P3
Why is the uniform distribution achieved finally?

## Slide 51
Run the code to see the final posterior distribution!
Red * 0.6
Green *0.2
Z
Red * 0.6
Green *0.2
Z
P3

## Slide 52
Run the code to see the final posterior distribution!
Red * 0.6
Green *0.2
Z
Red * 0.6
Green *0.2
Z
Green* 0.6
Red *0.2
Z
P3

## Slide 53
Implement robot motion…

## Slide 54
We know the robot moves to the right, and will assume the world is cyclic. So, when the robot reaches the right-most cell, it will circle around back to the first, or left-most cell.
1/9
1/3
1/3
1/9
1/9

## Slide 55
Assuming the robot moves exactly one position to the right, what is the probability distribution after the motion?
1/9
1/3
1/3
1/9
1/9

## Slide 56
Every grid shifts to the right one cell.
1/9
1/3
1/3
1/9
1/9
1/9
1/9
1/3
1/3
1/9
Let’s implement this！

## Slide 57
P4
Circular convolution

## Slide 58
1/9
1/3
1/3
1/9
1/9
1/9
1/9
1/3
1/3
1/9
Accurate motion
Let’s see inaccurate motion

## Slide 59
U = 1
U = 2
Assume the robot executes its action with high probability (0.8), correctly; with small probability (0.1) it will overshoot or undershoot. Note that this is a more accurate model of real robot motion.
0.1
0.8
0.1

## Slide 60
U = 2
It is the primary reason why localization is hard, because robots are not very accurate.
0.1
0.8
0.1
The distribution after the motion given a prior distribution:

## Slide 61
0
1
0
0
0
What is the distribution after motion?
U = 2

## Slide 62
0
1
0
0
0
0
0
0.1
0.8
0.1
As expected, the probability distribution has shifted and spread out. Moving causes a loss of information.
U = 2

## Slide 63
0
0.5
0
0.5
0
Let’s do this again for a different distribution. It is a cyclic motion model as before. What is the posterior?

## Slide 64
0
0.5
0
0.5
0
0
0
0.05
0.4
0.05
We answer this in the same way as in the previous question.
U = 2
Is this correct?

## Slide 65
0
0.5
0
0.5
0
We answer this in the same way as in the previous question, but this time we have to take into account that cell 5 can be arrived at in 2 ways: by cell 4 undershooting or cell 2 overshooting.
0.4
0.05
0.05
0.4
0.05
0.05
0.4
0.05
0.05
0.4
0.1
U = 2
Let’s implement this！

## Slide 66
P5

## Slide 67
0.2
0.2
0.2
0.2
0.2
0.2
0.2
0.2
0.2
0.2
U = 2
Realize that if we start with a uniform prior distribution (state of maximum confusion), and we then move, we MUST end up with the uniform distribution. Since this problem starts with a state of maximum confusion and then moves (which, remember, never increases our knowledge of the system), we must remain in the maximally confused state.

## Slide 68
1
0
0
0
0
What happens if the robot never senses but executes the motion to the right forever, what will be the limit or stationary distribution in the end?
U = 1
Let’s implement this！ Robot moves 100 steps without sensing.

## Slide 69
P6
p = [1, 0, 0, 0, 0];
u = 1;
step = 100;
pExact = 0.8;
pOvershoot = 0.1;
pUndershoot = 0.1;
for i = 1 : step
p = move(p, u, pExact, pOvershoot, pUndershoot);
disp(i);
disp(p);
end

## Slide 78
After 50 moves, we have lost essentially all information about the robot's location.
We need to be continuously sensing if we want to know the robot's location.

## Slide 79
1
0
0
0
0
0.2
0.2
0.2
0.2
0.2
It is uniform distribution!
U = 1
We can also solve for the probability of each cell by realizing that each cell is the possible destination for three other cells.

## Slide 80
Have you realized how crucial sensing is?

## Slide 81
Gain information
Lose information
Sense
Move
Initial belief

## Slide 82
Entropy
is a measure of the uncertainty in a random variable. In this context, the term usually refers to the Shannon entropy, which quantifies the expected value of the information contained in a message.
http://en.wikipedia.org/wiki/Entropy_(information_theory)
Entropy
Informative

## Slide 83
The Entropy when tossing coin
Assuming the probability of being head can be specified (0~1), what will the entropy be?
Let’s implement this！

## Slide 84
P65

## Slide 85
P65

## Slide 86
pHead = 0 : 0.01 : 1;
n = length(pHead);
H = zeros(1, n);
for i = 1 : n
p = [pHead(i), 1 - pHead(i)];
if (pHead(i) == 0)
p = 1 - pHead(i);
elseif 1 - pHead(i) == 0;
p = pHead(i);
end
H(i) = -sum(p .* log2(p) );
if mod(pHead(i), 0.1) == 0 && pHead(i)~= 0 && pHead(i) ~= 1
htemp = figure(1);
bar(p,1);
ylim([0,1]);
set(gca, 'XTickLabel', {'pHead', 'pTail'});
ylabel('Probability');
title(sprintf('pHead=%.2f, pTail=%.2f',pHead(i),1-pHead(i)));
colormap(cool);
print(htemp,'-dpng',sprintf('phead=%.2f.png', pHead(i)));
end
end
P65

## Slide 87
Which one is most informative?
Which one is most uncertain?

## Slide 88
Informative?
The most uncertain one
The most certain one

## Slide 89
0.4690
0.8813
1.0000

## Slide 90
0.4690
0.8813
1.0000
In an estimation-theoretic context
it is most natural to think of the “most informative” probability distribution as that which assigns all probability to a single state; logically the most compact of probabilities.
Conversely, the “least informative” distribution is one in which probability is spread uniformly over all states and so entropy is a maximum.
Maximum entropy distributions are often used as prior distributions when no useful prior information is available

## Slide 91
0.4690
0.8813
1.0000
In an estimation-theoretic context
it is most natural to think of the “most informative” probability distribution as that which assigns all probability to a single state; logically the most compact of probabilities.
Conversely, the “least informative” distribution is one in which probability is spread uniformly over all states and so entropy is a maximum.
Maximum entropy distributions are often used as prior distributions when no useful prior information is available
Most informative
Least informative
Entropy
Informative
Uncertainty

## Slide 92
0.4690
0.8813
1.0000
In a communication context
If the result of the experiment is known with high probability a priori, then the actual occurrence of the event is not very informative.
Conversely, if the possibility of each outcome is uniformly distributed, then the outcome itself is most informative.
The outcome of a random experiment is guaranteed to be most informative if the probability distribution over outcomes is uniform.

## Slide 93
0.4690
0.8813
1.0000
In a communication context
If the result of the experiment is known with high probability a priori, then the actual occurrence of the event is not very informative.
Conversely, if the possibility of each outcome is uniformly distributed, then the outcome itself is most informative.
The outcome of a random experiment is guaranteed to be most informative if the probability distribution over outcomes is uniform.
Most informative
Least informative
Entropy
Informative
Uncertainty

## Slide 94
Entropy
Informative
Uncertainty
Entropy
Informative
Uncertainty
In an estimation-theoretic context
In a communication context

## Slide 95
Entropy
Informative
Uncertainty
In an estimation-theoretic context
Localization complies with this rule!

## Slide 96
Entropy
Informative
Uncertainty
In an estimation-theoretic context
Let’s demonstrate the rule with robot motion!

## Slide 97
P7
entropy = zeros(1, step);
for i = 1 : step
p = move(p, u, pExact, pOvershoot, pUndershoot);
entropy(i) = -sum(p .* log2(p) );
disp(i);
disp(p);
end
h = figure(1);
hold on;
plot(1:step,entropy, '-','linewidth', 2,'color', 'g');
plot(1:step,entropy, '^','linewidth', 1.5,'color', 'r');
xlabel('Motion step');
ylabel('Entropy');
print(h, '-dpng', 'entropy.png');

## Slide 98
P7
Entropy
Informative
Uncertainty

## Slide 99
Which cell will robot be most probably next to after the two measurements and the two motions?
Z
Z
Where am I?
U = 1
U = 1

## Slide 100
Z
Z
I am probably here!
U = 1
U = 1
We find the robot most likely in right-most cell
Let’s implement this！

## Slide 101
p = [0.2, 0.2, 0.2, 0.2, 0.2]; % Prior
world = {'green', 'red', 'red', 'green', 'green'}; % Map
%% First configuration of meas. & motion
measurements = {'red', 'green'}; % Observation
motions = [1, 1];
%% Observation model
pHit = 0.6;
pMiss = 0.2;
%% Motion model / Process model
pExact = 0.8;
pOvershoot = 0.1;
pUndershoot = 0.1;
%% The recursive sensing and moving
entropy = zeros(2, length(motions));
for i = 1 : length(measurements)
%% Update by sensing
p = sense(p, measurements(i), world, pHit, pMiss);
entropy(1,i) = -sum(p .* log2(p) );
%% Predict by moving
p = move(p, motions(i), pExact, pOvershoot, pUndershoot);
entropy(2,i) = -sum(p .* log2(p) );
end
P8
First configuration

## Slide 102
0.2116 0.1516 0.0811 0.1684 0.3874
entropy(end, end) = 2.1433
P8

## Slide 103
P8
Entropy
Informative
Uncertainty
entropy(end, end) = 2.1433
Update
Predict
Predict

## Slide 104
world = {'green', 'red', 'red', 'green', 'green'};
measurements = {'red', 'green', 'green'};
motions = [1, 1, 1];
0.4118 0.2522 0.0761 0.0515 0.2085
entropy(end, end) = 2.0030
Second configuration

## Slide 105
world = {'green', 'red', 'red', 'green', 'green'};
measurements = {'green', 'red'};
motions = [1, 1];
entropy(end, end) = 2.1445
0.1400 0.1853 0.3884 0.2021 0.0842
Third configuration

## Slide 106
world = {'green', 'red', 'red', 'green', 'green'};
measurements = {'green', 'green'};
motions = [3, 1];
entropy(end, end) = 2.2329
Fourth configuration
0.1907 0.1645 0.1355 0.1645 0.3449

## Slide 107
world = {'green', 'red', 'red', 'green', 'green'};
measurements = {‘red', 'red'};
motions = [3, 1];
entropy(end, end) = 2.2783
Fifth configuration
0.1970 0.2149 0.2582 0.2149 0.1149

## Slide 108
world = {'green', 'red', 'red', 'green', 'green'};
measurements = {'red', 'red'};
motions = [2, 1];
entropy(end, end) = 2.2783
Sixth configuration
0.1970 0.1149 0.2149 0.2582 0.2149

## Slide 109
Configuration ID | Correctness | Sharpest peek of posterior | Final entropy | Visualization of posterior
First |  | 0.3874 | 2.1433 | 
Second |  | 0.4118 | 2.0030 | 
Third |  | 0.3884 | 2.1445 | 
Fourth |  | 0.3449 | 2.2329 | 
Fifth |  | 0.2582 | 2.2783 | 
Sixth |  | 0.2582 | 2.2783 | 

## Slide 110
The probability distribution we pursuit should have two qualities:
It should have one sharp peak. This indicates that the robot has a very specific belief about its current location.
The peak should be correct! If this weren't true, the car would believe--very strongly--that it was in the wrong location. This would be bad .

## Slide 111
That’s the essence of mobile robot localization!

## Slide 112
1. Start with a belief set about our current location.
2. Multiply this distribution by the results of our sense measurement.
3. Normalize the resulting distribution.
4. Move by performing a convolution. This sounds more complicated than it really is: this step really involved multiplication and addition to obtain the new probabilities at each
The localization procedure can be written as a series of steps:

## Slide 113
You may be curious about how we can use individual cells to represent a road. After all, a road isn't neatly divided into cells for us to jump between. Mathematically, we would say the road is not discrete it is continuous. Initially, this seems like a problem. Fortunately, whenever we have a situation where we don't need exact precision, we can chop a continuous distribution into pieces and make those pieces as small as we need.
To use continuous probability distributions to describe beliefs, we need Kalman filter-liked algorithms…

## Slide 114
Extend 1D to 2D

## Slide 115
Let’s model the 2D world as a set of colored cells.

## Slide 117
Motion commands:
[0, 0] Keep stationary
[0, 1] Move right
[0, -1] Move left
[1, 0] Move down
[-1, 0] Move up
It is also cyclic.

## Slide 118
[0, 0] Keep stationary
[0, 1] Move right
[0, -1] Move left
[1, 0] Move down
[-1, 0] Move up
The motion is executed correctly at a probability of 0.8. When the motion fails, the robot won’t move at all
Let’s implement this！

## Slide 119
world = {'red', 'green', 'green', 'red' , 'red';
'red', 'red', 'green', 'red', 'red';
'red', 'red', 'green', 'green', 'red';
'red', 'red', 'red', 'red', 'red'}; % Map
nRow = size(world, 1);
nCol = size(world, 2);
pStart = 0.7;
p = (1 - pStart) / (nRow * nCol-1) * ones(nRow, nCol);% Prior
p(3, 2) = pStart;
stop = [0, 0];
right = [0, 1];
left = [0,-1];
down = [1, 0];
up = [-1,0];
motions = {right};
pMoveCorrect = 0.8;
q = move(p, cell2mat(motions(1)), pMoveCorrect);
P9

## Slide 120
function q = move(p, u, pMoveCorrect)
nRow = size(p, 1);
nCol = size(p, 2);
q = zeros(nRow, nCol);
for r = 1 : nRow
for c = 1 : nCol
q(r, c) = pMoveCorrect * ...
p(mod(r-1-u(1), nRow) + 1, mod(c-1-u(2), nCol) + 1)...
+ (1 - pMoveCorrect) * p(r, c);
end
end
end
function [r, c] = maxMat(g)
% Find the index of the largest element of g
[temp,r] = max(g);
[~,c] = max(temp);
r = r(c);
end
P9

## Slide 121
The Prior:
0.0150 0.0150 0.0150 0.0150 0.0150
0.0150 0.0150 0.0150 0.0150 0.0150
0.0150 0.7000 0.0150 0.0150 0.0150
0.0150 0.0150 0.0150 0.0150 0.0150
The probability after moving:
0.0150 0.0150 0.0150 0.0150 0.0150
0.0150 0.0150 0.0150 0.0150 0.0150
0.0150 0.1520 0.5630 0.0150 0.0150
0.0150 0.0150 0.0150 0.0150 0.0150
The largest probability 0.5630 occurs at cell (3, 3)

## Slide 122
P9

## Slide 123
P9

## Slide 124
The Prior:
0.0150 0.0150 0.7000 0.0150 0.0150
0.0150 0.0150 0.0150 0.0150 0.0150
0.0150 0.0150 0.0150 0.0150 0.0150
0.0150 0.0150 0.0150 0.0150 0.0150
The probability after moving:
0.0150 0.0150 0.1520 0.0150 0.0150
0.0150 0.0150 0.0150 0.0150 0.0150
0.0150 0.0150 0.0150 0.0150 0.0150
0.0150 0.0150 0.5630 0.0150 0.0150
The largest probability 0.5630 occurs at cell (4, 3)

## Slide 127
The sensor measurement is correct at a probability of 0.7
Let’s implement this！

## Slide 128
function q = sense(p, z, world, pSenseCorrect)
nRow = size(p, 1);
nCol = size(p, 2);
q = zeros(nRow, nCol);
for r = 1 : nRow
for c = 1 : nCol
hit = strcmp(z, world(r, c));
q(r, c) = p(r, c) *...
(hit * pSenseCorrect + (1-hit) * (1 - pSenseCorrect));
end
end
q = q / sum(sum(q));
end
pSenseCorrect = 0.7;
q = sense(p, cell2mat(measurements(1)), world, pSenseCorrect);
measurements = {'green'};
P10

## Slide 129
The Prior:
0.0150 0.0150 0.0150 0.0150 0.0150
0.0150 0.0150 0.0150 0.0150 0.0150
0.0150 0.7000 0.0150 0.0150 0.0150
0.0150 0.0150 0.0150 0.0150 0.0150
The probability after sensing:
0.0138 0.0323 0.0323 0.0138 0.0138
0.0138 0.0138 0.0323 0.0138 0.0138
0.0138 0.6452 0.0323 0.0323 0.0138
0.0138 0.0138 0.0138 0.0138 0.0138
P10

## Slide 130
motions = {stop, right, down, down, right};
measurements = {'green', 'green', 'green' ,'green', 'green'};
Move
Sense
Which cell will robot be most probably at after these motions and measurements?

## Slide 131
motions = {stop, right, down, down, right};
measurements = {'green', 'green', 'green' ,'green', 'green'};
Move
Sense
The robot will be at cell (3, 4)
Let’s implement this！

## Slide 132
Move
Sense

## Slide 133
The Posterior:
0.0111 0.0246 0.0680 0.0447 0.0247
0.0072 0.0102 0.0870 0.0799 0.0094
0.0074 0.0089 0.1127 0.3535 0.0407
0.0091 0.0072 0.0143 0.0431 0.0364
The largest probability 0.3535 occurs at cell (3, 4)

## Slide 134
Entropy
Informative
Uncertainty
Update
Predict
P11

## Slide 135
P11
pMoveCorrect = 0.8;
pSenseCorrect = 0.7;
compEntropy = inline('-sum(sum(p .* log2(p)))'); % Inline function
p = 1 / (nRow * nCol - 1) * ones(nRow, nCol); % Prior
%% Fisrt configuration
motions = {stop, right, down, down, right};
measurements = {'green', 'green', 'green' ,'green', 'green'};
%% Check the size
if length(motions) ~= length(measurements)
error('The variable ''motions'' should be of the same size as ''measurements''!');
end
entropy = zeros(2, length(motions));
%% The main loop
for i = 1 : length(motions)
p = move(p, cell2mat(motions(i)), pMoveCorrect);
p0 = p;
p = sense(p, cell2mat(measurements(i)), world, pSenseCorrect);
%% Compute entropy
entropy(:, i) = [compEntropy(p0); compEntropy(p)];
end
%% Locate the final cell
[r, c] = maxMat(p);
fprintf('The largest probability %.4f occurs at cell (%d, %d)\n ',...
p(r,c), r, c);

## Slide 136
Histogram filter

## Slide 137
http://veterobot.com/
An open sourced and 3D printed robot
Histogram Demo

## Slide 138
Assignment 2
Give a presentation covering following topics:
  Bayes filter
  Mathematical derivation of Bayes filter
The talk shouldn’t be longer than 15 minutes.
Involving some coding-based simulations is better.
2. Preview/Review P1-P8 following this slides.

## Slide 139
Assignment 3
Give a presentation covering following topic:
  Circular convolution
The talk shouldn’t be longer than 15 minutes.
Involving some coding-based simulations is better.
2. Share your understanding of P8.