## Slide 1: The Fundamental of Mobile Robot
Machine Perception and Interaction Group (MPIG)
http://www.mpig.com.cn
szl@mpig.com.cn

## Slide 2
All the codes and slides accompanying the course are open-source
https://github.com/sunzuolei/robot
https://git.oschina.net/samuel/rob

## Slide 3
Geometry in Robotics

## Slide 4
@article{
author = {Smith, R. and Self, M. and Cheeseman, P.},
title = {Estimating uncertain spatial relationships in robotics},
journal = {Autonomous Robot Vehicles},
pages = {167-193},
year = {1990}
}

## Slide 8
What are the essential issues behind the demos?

## Slide 9
Coordinate frames
Spatial relationships
Transformation

## Slide 10
Suppose the robot starts from [A, B], then it moves C along x and D along y, where is the robot now?

## Slide 11
We can locate the robot at
Let us calculate it more elegantly.

## Slide 14
Compounding
head-to-tail

## Slide 15
Compounding

## Slide 16
Compounding

## Slide 28
Compounding
head-to-tail

## Slide 30
Transformation matrix
http://en.wikipedia.org/wiki/Transformation_matrix
Translation
Rotation

## Slide 31
World frame
Robot-centered frame
Robot-centered frame
Sensor-centered frame
Sensor-centered frame

## Slide 32
The coordinate of pose a is (5m, 3m, 50degree) ;
The pose b locates at
(4m, 2m, 20degree)
with respect to the robot-centered frame of pose a.
What is the coord. of pose b w.r.t world frame?

## Slide 33
The coordinate of pose a is (5m, 3m, 50degree) ;
The pose b locates at
(4m, 2m, 20degree)
with respect to the robot-centered frame of pose a.
What is the coord. of pose b w.r.t world frame?

## Slide 34
Compounding
head-to-tail
Let’s implement this!

## Slide 35
Xwa = [5; 3; degtorad(50)];
Xab = [4; 2; degtorad(20)];
Xwb = compound(Xwa, Xab);
fprintf('Xwb is (%.2fm, %.2fm, %.2fdegree)\n',...
Xwb(1), Xwb(2), radtodeg(Xwb(3)));
P22

## Slide 36
function Xwb = compound(Xwa, Xab)
rot = [cos(Xwa(3)) -sin(Xwa(3));
sin(Xwa(3)) cos(Xwa(3))];
Xwb(1:2,:) = rot * Xab(1:2,:) +
repmat(Xwa(1:2), 1, size(Xab,2));
%% if Xwb is a pose and not a point
if size(Xab,1) == 3
Xwb(3,:) = piTopi(Xwa(3,:) + Xab(3));
end
end
P22
Xab can be of size 3*n or 2*n

## Slide 37
The coordinate of pose a is (5m, 3m, 50degree) ;
Two features are sensed. Their coordinates in robot-centered frame are
(3m, 2.5m), (5m, 2m).
What are the coords. of feature f and d w.r.t world frame?

## Slide 38
The coordinate of pose a is (5m, 3m, 50degree) ;
Two features are sensed. Their coordinates in robot-centered frame are
(3m, 2.5m), (5m, 2m).
What are the coords. of feature f and d w.r.t world frame?

## Slide 39
Compounding
head-to-tail
Let’s implement this!

## Slide 40
Xwa = [5; 3; degtorad(50)];
Xad = [5; 2];
Xaf = [3; 2.5];
Xadf = [Xad, Xaf];
Xwd = compound(Xwa, Xad);
Xwf = compound(Xwa, Xaf);
Xwdf = compound(Xwa, Xadf);
%%
disp('Xwd = ');
disp(Xwd);
disp('Xwf = ');
disp(Xwf);
disp('Xwdf = ');
disp(Xwdf);
P23

## Slide 41
The coordinate of pose a is (5m, 3m, 50degree) ;
The pose b locates at
(4m, 2m, 20degree)
with respect to the robot-centered frame of pose a.
How can we visualize the robot body shape?
Let’s implement this!

## Slide 42
P24

## Slide 43
P24

## Slide 44
rob = [0 -3 -3;
0 -1 1] * 0.5;
%%
figure('name', 'Robot appearance')
patch(rob(1, :), rob(2, :), 'g');
axis equal;
box on;
print('-dpng', 'robotbody.png');
%%
Xwa = [5; 3; degtorad(50)];
Xab = [4; 2; degtorad(20)];
Xwb = compound(Xwa, Xab);
%%
robA = compound(Xwa, rob);
robB = compound(Xwb, rob);
P24

## Slide 45
figure('name', 'Visualization of robot body')
hold on;
axis equal;
grid minor;
xlim([0, 8]);
ylim([0, 8]);
pRobA = patch(robA(1, :), robA(2, :), [255,215,0]/255);
text(Xwa(1), Xwa(2), '\leftarrow X_{wa}', 'FontSize', 18);
pRobB = patch(robB(1, :), robB(2, :), [127,255,0]/255);
text(Xwb(1), Xwb(2), '\leftarrow X_{wb}', 'FontSize', 18);
P24
http://www.wahart.com.hk/rgb.htm
http://gucky.uni-muenster.de/cgi-bin/rgbtab-en
RGB Color Table

## Slide 46
Play with real data

## Slide 48
laser
2610 * 361
Laser point clouds
relMotion
3 * 2609
Relative motion
Translation and rotation
rose.mat

## Slide 49
Calculate the robot poses with rotation and translations
Let’s implement this!

## Slide 50
P25

## Slide 51
load '../data/rose.mat'
clear laser;
len = size(relMotion, 2);
rob = [0 -3 -3; 0 -1 1] * 0.5;
%% Initialize figure
figPos = get(0, 'ScreenSize'); % [left, bottom, width, height]
figPos(3) = figPos(3) - 100;
figure('name', 'Motion animation',...
'position', figPos,...
'color', 'w', 'Menu', 'none');
hold on; box on;
grid minor;
robPlot = patch(0, 0, 'b', 'erasemode', 'normal');
pathPlot = plot (0, 0, 'r-', 'linewidth', 5, 'erasemode','background');
xlabel('X(m)');
ylabel('Y(m)');
axis equal;
axis([-5 15 -5 15]);
P25

## Slide 52
pos = zeros(3, 1);
path = zeros(3, len + 1);
for i = 1 : len
pos = compound(pos, relMotion(:, i));
path(:, i+1) = pos;
robPos = compound(pos, rob);
set(robPlot, 'xdata', robPos(1, :), 'ydata', robPos(2, :));
set(pathPlot, 'xdata', path(1, 1:i), 'ydata', path(2, 1:i));
drawnow;
pause(0.005);
end
P25

## Slide 53
Make video with Matlab
Let’s implement this!
NOTE: The p26 employs the object VideoWriter and is debugged on Matlab 2013a, it might be not compatible with the version before 2011b.
P26

## Slide 54
%% Initialize vedio maker
videoObj = VideoWriter('robot.avi');
videoObj.FrameRate = 5;
videoObj.Quality = 100;
open(videoObj);
if mod(i, 6) == 0
frame = getframe;
writeVideo(videoObj, frame);
End
close(videoObj);
P26

## Slide 55
Cartesian VS. Polar
http://en.wikipedia.org/wiki/Cartesian_coordinate_system
http://en.wikipedia.org/wiki/Polar_coordinate_system

## Slide 56
Cartesian coordinate system
a coordinate system that specifies each point uniquely in a plane by a pair of numerical coordinates, which are the signed distances from the point to two fixed perpendicular directed lines, measured in the same unit of length.
Each reference line is called a coordinate axis or just axis of the system.
the point where they meet is its origin, usually at ordered pair (0, 0).

## Slide 57
Polar coordinate system
In which each point on a plane is determined by a distance from a fixed point and an angle from a fixed direction.
The fixed point (analogous to the origin of a Cartesian system) is called the pole, and the ray from the pole in the fixed direction is the polar axis. The distance from the pole is called the radial coordinate or radius, and the angle is the angular coordinate, polar angle, or azimuth.

## Slide 58
The coordinate of pose a is (5m, 3m, 50degree) ; The pose b’s displacement and rotation are 7m and 40degree w.r.t pose a’s robot-centered frame.
What is the coords. of b w.r.t world frame?

## Slide 59
The coordinate of pose a is (5m, 3m, 50degree) ; The pose b’s displacement and rotation are 7m and 40degree w.r.t pose a’s robot-centered frame.
What is the coords. of b w.r.t world frame?
Range
Bearing

## Slide 60
Transform Polar to Cartesian
Compound Xwa and Xab
Let’s implement this!

## Slide 61
path(path, genpath('../p22'));
Xwa = [5; 3; degtorad(50)];
disB = 7;
rotB = degtorad(40);
[xab, yab] = pol2cart(rotB, disB);
Xab = [xab; yab; rotB];
Xwb = compound(Xwa, Xab);
fprintf('Xwb is (%.2fm, %.2fm, %.2fdegree)\n',...
Xwb(1), Xwb(2), radtodeg(Xwb(3)));
P27

## Slide 62
Displacement
Displacement
Displacement
Rotation
Rotation
Rotation
Compounding
head-to-tail
Dead reckoning
http://en.wikipedia.org/wiki/Dead_reckoning

## Slide 63
Displacement
Displacement
Displacement
Rotation
Rotation
Rotation
Compounding
head-to-tail
Odometry

## Slide 64
Compounding
head-to-tail
Odometry
Encoder

## Slide 67
Visual Odometry

## Slide 69
A
B

## Slide 70
+
=

## Slide 71
1. Pixels selection
3. Pixels tracking
2. Stereovision
Stereovision
4. Motion
estimation

## Slide 72
仅基于视觉……

## Slide 75
Laser point clouds transformation

## Slide 80
Transform Polar to Cartesian
Compound Xwa and Xaf

## Slide 81
laser
2610 * 361
Laser point clouds
relMotion
3 * 2609
Relative motion
Translation and rotation
rose.mat

## Slide 82
load '../data/rose.mat'
Let’s visualize the data!

## Slide 83
P28

## Slide 84
for i = 1 : len
points = getLaserPoint(laser(i, :), maxR);
set(lsrFig, 'xdata', points(1,:), ...
'ydata', points(2, :));
title(sprintf('Laser image Frame %d', i));
drawnow;
if mod(i, 4) == 0 && vedio
frame = getframe;
writeVideo(videoObj, frame);
end
if vedio == 0
pause(0.02);
end
end
P28

## Slide 85
Combine the mapping and localization
P29

## Slide 86
for i = 1 : len
pos = compound(pos, relMotion(:, i));
path(:, i+1) = pos;
robPos = compound(pos, rob);
points = getLaserPoint(laser(i+1, :), maxR);
pointsWorld = compound(pos, points);
set(robPlot, 'xdata', robPos(1, :), 'ydata', robPos(2, :));
set(pathPlot, 'xdata', path(1, 1:i), 'ydata', path(2, 1:i));
set(lsrPlot, 'xdata', pointsWorld(1, :), ...
'ydata', pointsWorld(2, :));
plot(pointsWorld(1, 1: n : end), pointsWorld(2, 1: n : end),...
'.', 'markersize', 3, 'color', [169,169,169] / 255);
drawnow;
if mod(i, 6) == 0 && vedio
frame = getframe;
writeVideo(videoObj, frame);
end
end
P29

## Slide 87
Inversion

## Slide 88
The coordinate of pose b is (5m, 3m, 50degree) w.r.t pose a’s robot-centered frame.
What is the coords. of a w.r.t the robot-centered frame of b?

## Slide 90
Transformation matrix
http://en.wikipedia.org/wiki/Transformation_matrix
Translation
Rotation

## Slide 92
Compounding
Inversion
Section 3.2.2
[Smith 1990]
Let’s prove it by programming!

## Slide 93
syms t x y t;
X = [x; y; t];
negX = -X;
R = [ cos(negX(3)), -sin(negX(3)), 0;
sin(negX(3)), cos(negX(3)), 0;
0, 0, 1];
invR = [ -cos(X(3)), -sin(X(3)), 0;
sin(X(3)), -cos(X(3)), 0;
0, 0, -1];
r1 = R * negX;
r2 = invR * X;
r3 = r1 - r2;
%%
disp('R * (-X) is:');
disp(r1);
disp('inv(R) * X is:');
disp(r2);
P30

## Slide 94
Inversion
Section 3.2.2
[Smith 1990]
Let’s prove it by programming!

## Slide 95
Xab = [96; 35; degtorad(62)];
Xba = inverse(Xab);
Xab_ = inverse(Xba);
Xab_(3) = radtodeg(Xab_(3));
disp(Xab_);
function Xba = inverse(Xab)
if size(Xab, 1) ~= 3 || size(Xab, 2) ~= 1
error('Xab should be of the size 3*1');
end
R = [ -cos(Xab(3)), -sin(Xab(3)), 0;
sin(Xab(3)), -cos(Xab(3)), 0;
0, 0, -1];
Xba = R * Xab;
Xba(3) = piTopi(Xba(3));
end
P31

## Slide 96
Let’s implement this!

## Slide 97
path(path, genpath('../p31'));
Xab = [5; 3; degtorad(50)];
Xba = inverse(Xab);
disp('Xba = ')
disp(Xba);
P32

## Slide 98
Composite relationships

## Slide 99
The coordinate of pose b is (5m, 3m, 50degree) w.r.t pose a’s robot-centered frame. The world coordinate of pose b is (9m, 6m, 70degree).
What is the coords. of a w.r.t the world frame?

## Slide 101
Is this the unique solution?

## Slide 102
Let’s prove it by programming!

## Slide 103
path(path, genpath('../p31'));
path(path, genpath('../p22'));
%%
Xab = [5; 3; degtorad(50)];
Xwb = [9; 6; degtorad(70)];
%% First solution
Xba = inverse(Xab);
Xwa = compound(Xwb, Xba);
disp('Fisrt solution: ')
disp(Xwa);
%% Second solution
Xwa2 = inverse(compound(Xab, inverse(Xwb)));
disp('Second solution: ')
disp(Xwa2);
P33

## Slide 104
Bicycle motion model
Courtesy of 许亚芳

## Slide 105
The vehicle performs a continuous movement. To analyze its movement, the derivations are required.
Path dynamics
Translation
Rotation
angular derivation (angular velocity)
displacement derivation
(velocity)

## Slide 106
Wheel-base
Reference point
simplification
Front wheel
Rear wheel

## Slide 107
equivalent
2-wheel
4-wheel

## Slide 108
Path dynamics

## Slide 109
How to compute Angular Velocity?
Path dynamics

## Slide 110
Circular motion
r

## Slide 111
Angular velocity

## Slide 112
discrete-time vehicle motion

## Slide 113
Motion Model

## Slide 114
velocity
steering

## Slide 115
velocity
steering

## Slide 116
Generate path
Based on the way points

## Slide 117
Now we consider the waypoint without direction!

## Slide 118
This angle must be kept within a certain range to keep balance !
If the vehicle wants to go to the next point, it must turn 50 degree to get there. Obviously, it has exceed its max degree (we assume the max degree is 20 degree)
How to deal with this situation ?

## Slide 119
2
5
2
2
2
1

## Slide 120
Turn steering
Steering < maxG ?
Turn maxG
N
Y
Go on

## Slide 121
Compute steering
Rate control
Angular control
Let’s learn how to implement it !
Summary

## Slide 122
P34

## Slide 123
Close all;clear all;clc;
Path(path, genpath(‘..\..\robotcourse));
load '../data/tim.mat'
clear lm;
steering=0;velocity=4.0;wheelbase=8;dt=0.05;iWp=1;iPos=1;
rob = [0 -wheelbase -wheelbase; 0 -4 4] ;
%% Initialize figure
figPos = get(0, 'ScreenSize');
figPos(3) = figPos(3) - 100;
figure('name', 'Motion animation',...
'position', figPos,...
'color', 'w', 'Menu', 'none');
hold on; box on;
grid minor;
robPlot = patch(0, 0, 'b', 'erasemode', 'normal');
pathPlot = plot (0, 0, 'r-', 'linewidth', 5, 'erasemode','background');
xlabel('X(m)');
ylabel('Y(m)');
axis equal;
axis([-110 100 -110 100]);
P34

## Slide 124
pos = zeros(3, 1);
path = zeros(3, 3390);
%% Main loop
while iWp ~= 0
[steering,iWp]= compSteer(pos, wp, iWp, steering,dt);
pos(1) = pos(1) + velocity *dt *cos(steering +pos(3,:));
pos(2) = pos(2) + velocity *dt *cos(steering +pos(3,:));
pos(3) = pos(3) + velocity *dt *sin(steering)/wheelbase;
pos(3) = piTopi(pos(3));
robPos = compound(pos,rob);
path(:, iPos + 1)= pos;
iPos = iPos + 1;
%%
set(pathPlot,'xdata', path(1, 1:iPos),'ydata',
path(2,1:iPos));
set(robPlot,'xdata',robPos(1,:),'ydata',robPos(2,:));
drawnow;
end
Print(‘-dpng’,’path.png’)
P34

## Slide 125
function [G,iwp]= compSteer(x,wp,iwp,G,dt)
maxG= 30*pi/180; rateG= 20*pi/180; minD = 0.5;
cwp= wp(:,iwp);
d2 = (cwp(1)-x(1))^2 + (cwp(2)-x(2))^2;
if d2 < minD^2
iwp = iwp+1; % switch to next
if iwp > size(wp,2) %reached final waypoint,return
iwp =0;return;
end
cwp= wp(:,iwp); % next waypoint
end
deltaG= piTopi(atan2(cwp(2)-x(2),cwp(1)-x(1))-x(3)-G);
% limit rate
maxDelta = rateG*dt;
if abs(deltaG) > maxDelta
deltaG = sign(deltaG)*maxDelta;
end
% limit angle
G= G+deltaG;
if abs(G) > maxG
G= sign(G)*maxG;
end
P34
compSteer