## Slide 1: The Fundamental of Mobile Robot
Machine Perception and Interaction Group (MPIG)
assignments.shmtu@gmail.com

## Slide 2
Send an email with specified subject ‘Robot stuff’ to
assignments.shmtu@gmail.com
An automatic reply will come.
All you need would be included!

## Slide 3
assignments.shmtu@gmail.com

## Slide 4
https://github.com/sunzuolei/robotcourse
All the codes accompanying this course are open-sourced at Github.
The project homepage:
https://github.com/sunzuolei/robotcourse.git
The git repository:
Learn more about git:
http://en.wikipedia.org/wiki/Git_(software)
https://code.google.com/p/tortoisegit/
The best GUI-based git client on Windows:

## Slide 5
Kalman
Filter
Rudolf (Rudy) Emil Kálmán
May 19, 1930–
A Hungarian-American electrical engineer, mathematical system theorist
http://en.wikipedia.org/wiki/Rudolf_E._K%C3%A1lm%C3%A1n

## Slide 6
@article{
Author = {Kalman, Rudolph Emil},
  Title = {A New Approach to Linear Filtering and Prediction Problems},
  Journal = {Transactions of the ASME--Journal of Basic Engineering},
  Volume = {82},
  Number = {Series D},
  Pages = {35--45},
  Year = {1960} }

## Slide 7
Prediction
Update
Innovation / Residual
Innovation variance
Kalman gain
Linear Kalman filter

## Slide 8
Linear models
Linear motion model
Linear sensor model

## Slide 9
The assumptions that observation are linear functions of the state and that the next state is a linear function of the previous state are crucial for the correctness of a linear Kalman filter.
Linear assumption

## Slide 10
The linear transformation of a Gaussian random variable results in another Gaussian random variable.

## Slide 11
ND
Nice properties of Gaussian distribution

## Slide 15
Is linear KF adequate for real applications?
NO!

## Slide 16
General Nonlinear models
Nonlinear motion model
Nonlinear sensor model

## Slide 17
The Nonlinear transformation of a Gaussian results in …

## Slide 20
Expensive!

## Slide 21
Prediction
Update
Innovation / Residual
Innovation variance
Kalman gain
Linear Kalman filter

## Slide 22
To maintain the Gaussian assumption, We require the transition matrices, then the LKF formulas can be reused, but HOW…

## Slide 23
Nonlinear
Linear
Linearization

## Slide 24
From LKF to EKF

## Slide 25
Taylor Expansion
A Taylor series is a series expansion of a function about a point. A one-dimensional Taylor series is an expansion of a real function f(x) about a point x=a is given by

## Slide 26
Where should the f’ be evaluated?

## Slide 27
Mean + Covariance

## Slide 28
Prediction
Linear Kalman filter

## Slide 29
Prediction
Linear Kalman filter

## Slide 30
Prediction
Linear Kalman filter

## Slide 31
Prediction
Linear Kalman filter

## Slide 32
Prediction
Extended
Kalman filter

## Slide 33
Mean + Covariance

## Slide 34
Linear Kalman filter

## Slide 35
Linear Kalman filter

## Slide 36
Prediction
Update
Innovation / Residual
Innovation variance
Kalman gain
Extended
Kalman filter

## Slide 37
The Jacobian matrix of function f with respect to x evaluated at \mu_{x_t}
The Jacobian matrix of function h with respect to x evaluated at \bar{\mu}_{x_{t+1}}

## Slide 38
Jacobian matrix
In vector calculus, the Jacobian matrix is the matrix of all first-order partial derivatives of a vector-valued function.

## Slide 39
Bearing-only sensor

## Slide 40
Calculate the Jacobian matrix of the following observation model w.r.t the state vector x:
Calculate it by programming!

## Slide 41
syms x y vx vy xs ys
h = atan((y - ys) / (x - xs));
X = [x, vx, y, vy];
H = jacobian(h, X);
disp(H);
P48
[ -(y - ys)/((x - xs)^2*((y - ys)^2/(x - xs)^2 + 1)), 0, 1/((x - xs)*((y - ys)^2/(x - xs)^2 + 1)), 0]
Just build the function jacobH using the result.

## Slide 42
http://www.mathworks.cn/cn/help/matlab/matlab_oop/scoping-classes-with-packages.html
function H = jacobH(Xs, X)
xs = Xs(1);
ys = Xs(2);
x = X(1);
y = X(2);
H = [ -(y - ys)/((x - xs)^2*((y - ys)^2/(x - xs)^2 + 1)), ...
0,...
1/((x - xs)*((y - ys)^2/(x - xs)^2 + 1)),...
0];
end
P49
Packages in Matlab
Namespace in C++
Packages Create Namespaces

## Slide 43
Partial nonlinearity

## Slide 44
Motion model
F
E
B
linear

## Slide 45
Measurement
model
nonlinear

## Slide 46
function z = sensorModel(x, sensorPos)
z = atan((x(2)-sensorPos(2))/(x(1)-sensorPos(1)));
if (x(1) - sensorPos(1)) < 0
z = piTopi( z + pi);
end
end
Measurement
model

## Slide 47
function z = sensorModel(x, sensorPos)
z = atan2( x(2)-sensorPos(2), x(1)-sensorPos(1) );
end
Measurement
model
Four-quadrant inverse tangent, it uses sign(Y) and sign(X) to determine the specific quadrant
atan2

## Slide 48
Motion model
Sensor model

## Slide 49
Update
Innovation / Residual
Innovation variance
Kalman gain
Prediction
nonlinear
linear

## Slide 50
P49

## Slide 52
for i = 1 : step
if i ~= 1
[mu, Sigma] = predictLKF(mu, Sigma, F, Q, ...
'processNoiseMat', E, 'controlMat', B,...
'control', u(:, i));
muPred(:,i) = mu;
SigmaPred(:,:,i) = Sigma;
end
H = p49.jacobH(mu, sensorPos);
[mu, Sigma, innov(:,i), SigmaInnov(:,:,i)] =...
updateEKF(mu, Sigma, @p49.sensorModel, sensorPos,...
zTrue(:,i), H, R, true, 1);
muPost(:,i) = mu;
SigmaPost(:,:,i) = Sigma;
end
P49

## Slide 53
function [muPost, SigmaPost, Y, S, K] = updateEKF(mu, Sigma,...
sensorModel, sensorPos, z, H, R, hasAngle, idxAngle)
%%
if nargin < 8
hasAngle = false;
end
if nargin == 8
idxAngle = length(z);
end
%%
Y = z - sensorModel(mu, sensorPos);
if hasAngle
Y(idxAngle) = piTopi(Y(idxAngle));
end
S = H * Sigma * H' + R;
K = Sigma * H' / S;
muPost = mu + K * Y;
SigmaPost = Sigma - K * S * K';
end
P49

## Slide 54
http://veterobot.com/
An open sourced and 3D printed robot
KF Demo with sonar

## Slide 55
0=2pi problem

## Slide 56
Prediction
Update
Innovation / Residual
Innovation variance
Kalman gain
Extended
Kalman filter

## Slide 57
Innovation / Residual
It is tricky if the measurement vector contains angles

## Slide 59
No! the angle A and B are actually very close, since 0=2pi.

## Slide 60
Correct solution:

## Slide 63
function angle = piTopi(angle)
% Input: array of angles.
% Output: normalised angles.
% Tim Bailey 2000, modified 2005.
% Samuel modifies it to bound the angle at
% [-pi, pi).
twopi = 2*pi;
angle = angle - twopi*fix(angle/twopi); % this is a stripped-down version of rem(angle, 2*pi)
i = find(angle >= pi); % Samuel modifies.
angle(i) = angle(i) - twopi;
i = find(angle < -pi);
angle(i) = angle(i) + twopi;
end

## Slide 65
Always bound the resulting angles using function piTopi.
General solution to 0=2pi problem

## Slide 66
%% Process noise sigma
sigmaCxNoise = 0.02;
sigmaCyNoise = 0.02;
%% Measurement noise sigma
sigmaBNoise = degtorad(0.09);
P50
Version SHA-1: ee267033a0

## Slide 67
%% Process noise sigma
sigmaCxNoise = 0.02;
sigmaCyNoise = 0.02;
%% Measurement noise sigma
sigmaBNoise = degtorad(0.09);
Version SHA-1: ee267033a0

## Slide 68
%% Process noise sigma
sigmaCxNoise = 0.02;
sigmaCyNoise = 0.02;
%% Measurement noise sigma
sigmaBNoise = degtorad(0.09);
Version SHA-1: ee267033a0

## Slide 70
Fully nonlinear demo

## Slide 71
Motion model

## Slide 72
Motion model

## Slide 73
Motion model

## Slide 74
Motion model

## Slide 75
Jacobian matrix
In vector calculus, the Jacobian matrix is the matrix of all first-order partial derivatives of a vector-valued function.

## Slide 87
Motion model
nonlinear

## Slide 88
Motion model
nonlinear

## Slide 89
Measurement
model
nonlinear
Calculate the Jacobians by programming!

## Slide 90
syms x y theta dx dy dtheta xs ys;
f = [dx * cos(theta) - dy * sin(theta) + x;
dy * cos(theta) + dx * sin(theta) + y;
dtheta + theta];
X = [x, y, theta];
F = jacobian(f, X);
disp(F);
simplify(F)
%%
h = atan((y - ys) / (x - xs));
H = jacobian(h, X);
disp(H);
simplify(H)
P52
[ 1, 0, - dy*cos(theta) - dx*sin(theta)]
[ 0, 1, dx*cos(theta) - dy*sin(theta)]
[ 0, 0, 1]
[ -(y - ys)/((x - xs)^2*((y - ys)^2/(x - xs)^2 + 1)),
1/((x - xs)*((y - ys)^2/(x - xs)^2 + 1)),
0]

## Slide 91
[ 1, 0, - dy*cos(theta) - dx*sin(theta)]
[ 0, 1, dx*cos(theta) - dy*sin(theta)]
[ 0, 0, 1]
[ -(y - ys)/((x - xs)^2*((y - ys)^2/(x - xs)^2 + 1)),
1/((x - xs)*((y - ys)^2/(x - xs)^2 + 1)),
0]
Construct the Jacobian matrix calculating function based on the syms formulas.

## Slide 92
function F = jacobF(X, u)
theta = X(3);
dx = u(1);
dy = u(2);
F = [1, 0, - dy*cos(theta) - dx*sin(theta);
0, 1, dx*cos(theta) - dy*sin(theta);
0, 0, 1];
end
P54/+p54/jacobF
[ 1, 0, - dy*cos(theta) - dx*sin(theta)]
[ 0, 1, dx*cos(theta) - dy*sin(theta)]
[ 0, 0, 1]

## Slide 93
function H = jacobH(X, Xs)
xs = Xs(1);
ys = Xs(2);
x = X(1);
y = X(2);
H = [ -(y - ys)/((x - xs)^2*((y - ys)^2/(x - xs)^2 + 1)), ...
1/((x - xs)*((y - ys)^2/(x - xs)^2 + 1)), ...
0];
end
P54/+p54/jacobH
[ -(y - ys)/((x - xs)^2*((y - ys)^2/(x - xs)^2 + 1)),
1/((x - xs)*((y - ys)^2/(x - xs)^2 + 1)),
0]

## Slide 94
The robot motion has been implemented in p25.
P53 simulates the bearing only observation based on the motions.
P53

## Slide 95
P53

## Slide 96
P54

## Slide 97
A general function predictEKF is constructed and the updateEKF produced for the partial nonlinear demo is reused here. To understand tricks employed in visualization sections, please study Matlab help documents. The programming style, variable structures and most of the codes can be reused in your future applications.
P54

## Slide 98
%% Tune noises
proNoiseScalar = 1.0;
obsNoiseScalar = 1.0;
%% Process noise sigma
sigmaXNoise = 0.00001;
sigmaYNoise = 0.00001;
sigmaThetaNoise = degtorad(0.0001);
Q = diag(proNoiseScalar * ...
[sigmaXNoise, sigmaXNoise, sigmaXNoise]).^2;
P55
The results are produced by the version (SHA-1: a3f036df, Date: 2013/6/13) in the git repository

## Slide 99
The results are produced by the version (SHA-1: a3f036df, Date: 2013/6/13) in the git repository

## Slide 100
The results are produced by the version (SHA-1: a3f036df, Date: 2013/6/13) in the git repository

## Slide 101
The results are produced by the version (SHA-1: a3f036df, Date: 2013/6/13) in the git repository

## Slide 102
The above three figures depict the consistency validation results with the approaches designed for linear Kalman filter. Something might be wrong here. Please revalue the performance and study related references, then get the elegant methods, suitable model configurations or (and) reasonable interpretations for the demo’s consistency.
P55

## Slide 103
Yes. Bugs do exist in the version before SHA-1: a3f036df. The Jacobian matrix used in prediction was definitely wrong!

## Slide 107
Please note that the linearization itself introduces error, so the estimation deviation is not zero even if noises are set to zero.
P55

## Slide 108
EKF Demo with Bearing & range

## Slide 109
Motion model
nonlinear

## Slide 110
Motion model
nonlinear

## Slide 111
Measurement
model
nonlinear
Calculate the Jacobians by programming!

## Slide 112
syms x y theta xs ys;
X = [x y theta];
%%
h = [atan((y - ys) / (x - xs)),...
sqrt((x-xs)^2 + (y-ys)^2)];
H = jacobian(h, X);
disp(H);
simplify(H)
P56
[ -(y - ys)/((x - xs)^2*((y - ys)^2/(x - xs)^2 + 1)), 1/((x - xs)*((y - ys)^2/(x - xs)^2 + 1)), 0]
[ (x - xs)/((x - xs)^2 + (y - ys)^2)^(1/2), (y - ys)/((x - xs)^2 + (y - ys)^2)^(1/2), 0]
[ -(y - ys)/((x - xs)^2*((y - ys)^2/(x - xs)^2 + 1)), 1/((x - xs)*((y - ys)^2/(x - xs)^2 + 1)), 0]
[ (2*x - 2*xs)/(2*((x - xs)^2 + (y - ys)^2)^(1/2)), (2*y - 2*ys)/(2*((x - xs)^2 + (y - ys)^2)^(1/2)), 0]
simplified

## Slide 113
P57

## Slide 114
P58

## Slide 115
P58

## Slide 116
P58

## Slide 117
KF for more general models

## Slide 118
Motion model
Sensor model

## Slide 119
Motion model
Sensor model

## Slide 120
Prediction
Update
Innovation / Residual
Innovation variance
Kalman gain
Linear Kalman filter

## Slide 121
Motion model
Sensor model

## Slide 122
Prediction
Update
Innovation / Residual
Innovation variance
Kalman gain
Linear Kalman filter

## Slide 123
Motion model
Sensor model

## Slide 124
Prediction
Update
Innovation / Residual
Innovation variance
Kalman gain
Extended
Kalman filter

## Slide 125
Motion model
Sensor model

## Slide 126
Prediction
Update
Innovation / Residual
Innovation variance
Kalman gain
Extended
Kalman filter

## Slide 127
The Jacobian matrix of function f with respect to x evaluated at \mu_{x_t}
The Jacobian matrix of function h with respect to x evaluated at \bar{\mu}_{x_{t+1}}
The Jacobian matrix of function f with respect to w evaluated at \mu_{x_t}
The Jacobian matrix of function h with respect to v evaluated at \bar{\mu}_{x_{t+1}}

## Slide 128
Bottlenecks of EKF

## Slide 129
EKF approximates state transitions and measurements using Taylor expansions, The goodness of the linear approximation depends on two main factors:
The degree of uncertainty
The degree of local nonlinearity of the functions that are being approximated.

## Slide 132
Higher uncertainty typically results in less accurate estimates of the mean and covariance of resulting random variable.

## Slide 135
Higher nonlinearities result in larger approximation errors.