## Slide 1: The Fundamental of Mobile Robot
Machine Perception and Interaction Group (MPIG)
http://www.mpig.com.cn
szl@mpig.com.cn

## Slide 2
Send an email with specified subject ‘Robot stuff’ to
assignments.shmtu@gmail.com
An automatic reply will come.
All you need would be included!

## Slide 3
assignments.shmtu@gmail.com

## Slide 4
https://github.com/sunzuolei/robotcourse
All the codes accompanying this course are open-sourced at Github.
The project homepage:
https://github.com/sunzuolei/robotcourse.git
The git repository:
Learn more about git:
http://en.wikipedia.org/wiki/Git_(software)
https://code.google.com/p/tortoisegit/
The best GUI-based git client on Windows:

## Slide 5
Information
Filter
Hugh Durrant-Whyte

## Slide 6
Canonical representation of Gaussian

## Slide 7
The standard parameterization of Gaussian:
As the covariance matrix is symmetrical, the two components are the same.
Let’s prove this by programming!

## Slide 8
a = 1; b = 2; c = 3; d = 4; e = 5; f = 6; g = 7;
mu = [a b]';
invSigma = [ c d;
d e ];
x = [f g]';
first = mu' * invSigma * x ;
second = x' * invSigma * mu ;
disp(first);
disp(second);
P68
As the covariance matrix is symmetrical, the two components are the same.

## Slide 9
The standard parameterization of Gaussian:

## Slide 10
The canonical parameterization of the multivariate Gaussian:
Information matrix
Precision matrix
Information vector
Fisher information

## Slide 11
From Linear KF to Linear
Information Filter
Mathematical Derivation of the Information Filter

## Slide 12
Kalman filter
Information filter
The dual of KF

## Slide 13
Linear models
Linear motion model
Linear sensor model

## Slide 14
Prediction
Update
Innovation / Residual
Innovation variance
Kalman gain
Linear Kalman filter

## Slide 15
Prediction
Linear Kalman filter
Linear Information filter
Information matrix
Precision matrix
Information vector

## Slide 16
Prediction
Linear Kalman filter
Linear Information filter
Information matrix
Precision matrix
Information vector

## Slide 17
As to the derivation of linear information filter update, please recall how we got the update routine of linear Kalman filter:

## Slide 18
Sensor model

## Slide 19
Sensor model

## Slide 20
Sensor model

## Slide 21
Sensor model
Is the distribution the Posterior?

## Slide 22
The information about the Posterior can be divided into two pieces:
Indicates the information from involving observations
Indicates the information from prediction

## Slide 23
With information matrix (Fisher information), the total information of posterior can be formulated as:
Information matrix

## Slide 24
Indicates the information from prediction
With information matrix (Fisher information), the total information of posterior can be formulated as:

## Slide 25
Indicates the information from involving observations
With information matrix (Fisher information), the total information of posterior can be formulated as:

## Slide 27
The mean of the posterior is the weighted sum of the mean values of the two Gaussian distributions. The weights are decided by the proportion of information contained in each of the Gaussian distributions.
Indicates the information from involving observations
Indicates the information from prediction

## Slide 28
The mean of the posterior is the weighted sum of the mean values of the two Gaussian distributions. The weights are decided by the proportion of information contained in each of the Gaussian distributions.

## Slide 29
Indicates the information from involving observations

## Slide 30
Prediction
Update
Linear Information Filter
State recovery

## Slide 31
Implement LIF based on the LKF demo
P39
P66

## Slide 32
P66

## Slide 33
function [xiPred, OmegaPred] = predictLIF(xi, Omega, F, Q, varargin)
%% Linear information filter prediction
if hasE
OmegaPred = eye(xiLen) / ( F / Omega * F' + E * Q * E' );
% Use '/' instead of 'inv' for efficiency
else
OmegaPred = eye(xiLen) / ( F / Omega * F' + Q );
end
if hasU
xiPred = OmegaPred * ( F / Omega * xi + B * u );
else
xiPred = OmegaPred * ( F / Omega * xi );
end
end
P66
Prediction

## Slide 34
function [xiPost, OmegaPost] = updateLIF(xi, Omega, z, H, R)
xiPost = H'/ R * z + xi;
OmegaPost = H'/ R * H + Omega;
end
P66
Update

## Slide 35
%%
path(path, '../p39'); % For LKF demo
path(path, '../p66'); % For LIF demo
%%
p39
save('lkftime.mat', 'timePredLKF', 'timeUpdateLKF');
%%
p66
save('liftime.mat', 'timePredLIF', 'timeUpdateLIF');
%%
clear all;
load lkftime.mat
load liftime.mat
P67
Compare the time costs
The NAÏVE linear information filter is generally more computationally expensive than LKF!

## Slide 36
%%
updateStart = tic;
[xi, Omega] = updateLIF(xi, Omega, zTrue(:,i), H, R);
  %% State recovery
  muPost(:,i) = Omega \ xi;
  timeUpdateLIF(i) = toc(updateStart);
P67
Compare the time costs
The time cost of state recovery is also taken into account.
Intel Core i5-2450M @ 2.50GHz, DDR3 1333MHz 8G

## Slide 37
P67

## Slide 38
From Linear IF to Extended IF
Mathematical Derivation of the Extended Information Filter

## Slide 39
General Nonlinear models
Nonlinear motion model
Nonlinear sensor model

## Slide 40
Taylor Expansion
A Taylor series is a series expansion of a function about a point. A one-dimensional Taylor series is an expansion of a real function f(x) about a point x=a is given by

## Slide 41
Mean + Covariance

## Slide 42
Prediction
Linear Information filter

## Slide 43
Prediction
Linear Information filter

## Slide 44
Prediction
Linear Information filter

## Slide 45
Prediction
Linear Information filter

## Slide 46
Mean + Covariance

## Slide 47
Linear information filter
Update

## Slide 48
Linear information filter
Update

## Slide 49
Prediction
Update
Extended Information Filter

## Slide 50
Prediction
The need to recover the sate estimate and state prediction stem from:
Jacobian matrix calculation
The system is represented by state vector

## Slide 51
Prediction
Update
Extended Information Filter
(The optimized routine)

## Slide 52
Covariance matrix
Implies how uncertain the estimate is
Initialized as infinite
Information matrix
Implies how certain the estimate is
Initialized as zero
The information filter tends to be numerically more stable than the Kalman filter in many of the robotics applications.

## Slide 53
Information filter enables a robot to integrate information without immediately resolving it into probabilities.
The information matrix and information vector in measurement update are additive.
This can be of great advantage in complex estimation problems, involving hundreds or even millions of variables.
It naturally fits multi-robot problems which often involve the integration of sensor data collected decentrally.
Update

## Slide 54
A primary disadvantage of the EIF is the need to recover a state estimate in the update step
Further matrix inversions are required for the prediction step of the information filters.
The EKF does not involve the inversion of matrices of comparable size.
For high dimensional state spaces, the information filter is generally believed to be computationally inferior to the Kalman filter.
This is one of the reasons why the EKF has been vastly more popular than the EIF.
Prediction

## Slide 55
Information filters can be thought of as graphs
States are connected whenever the corresponding off-diagonal element in the information matrix is non-zero.
Sparse information matrices correspond to sparse graphs; in fact, such graphs are commonly known as Gaussian Markov random fields.

## Slide 56
Implement EIF based on the EKF demo (bearing-only)
P54
P69

## Slide 57
P69

## Slide 58
function [muPred, xiPred, OmegaPred] = predictEIF(...
mu, Omega, u, motionModel, F, Q)
n = length(mu);
muPred = motionModel(mu, u);
OmegaPred = eye(n) / (F / Omega * F' + Q);
xiPred = OmegaPred * muPred;
end
P69
Prediction

## Slide 59
function [muPost, OmegaPost, xiPost] = updateEIF(mu, Omega, xi,...
sensorModel, sensorPos, z, H, R, hasAngle, idxAngle)
Y = z - sensorModel(mu, sensorPos) + H * mu;
if hasAngle
Y(idxAngle) = piTopi(Y(idxAngle));
end
xiPost = H' / R * Y + xi;
OmegaPost = H' / R * H + Omega;
muPost = OmegaPost \ xiPost;
P69
Update

## Slide 60
for i = 1 : step
if i ~= 1
u = relMotion(:, i-1);
predStart = tic;
F = p54.jacobF(mu, u);
[mu, xi, Omega] = predictEIF(mu, Omega, u,...
@p54.motionModel, F, Q);
timePredEIF(i) = toc(predStart);
%
end
H = p54.jacobH(mu, sensorPos);
updateStart = tic;
[mu, Omega, xi] =...
updateEIF(mu, Omega, xi, @p54.sensorModel, sensorPos,...
zTrue(:,i), H, R, true, 1);
timeUpdateEIF(i) = toc(updateStart);
end
P69

## Slide 61
Initalization
Although the information matrix can be in principle initialized to zero, the too small numerical initialization, e.g. 1e-8 * eye(3), might result in closely singular matrices during prediction or update, then the warnings like ‘Matrix is close to singular or badly scaled. Results may be inaccurate’ will be emitted.
As a rule of thumb, the information matrix should be initialized reasonably, the elements are not necessarily too close to zero. In p69, I feed ‘OmegaInit’ 1e-3 * eye(3) which implies that we are somewhat sure the robot’s initial state as the first batch of raw observations is adequately for ‘OmegaInit’ determination.
Similarly, the robot state can not be initialized to [0, 0, 0] to avoid the bad condition number with respect to matrix inversion.
P69

## Slide 62
Stability
The EIF demo shown in p69 seems to be more stable than the analogous EKF demo implemented in p54…
Strict performance comparison, as the future work, is needed to draw the above conclusion.
P69

## Slide 63
Implement EIF based on the EKF demo (bearing-range)
P57
P70

## Slide 64
Motion model
nonlinear

## Slide 65
Measurement
model
nonlinear
Calculate the Jacobians by programming!

## Slide 66
P70

## Slide 67
p70.m
p70InitFigure.m
reusability
Thanks to p57 and p69, the EIF demo with range & bearing sensor model can be built within 10 minutes!
It proves, once again, how important to keep reusability in your mind when programming!
The models and filtering functions are just borrowed from the existing codes by involving their path .
P70